# Advantages Reddi-Wall Has Over Other Fine ICF Systems

- Reddi–Wall has an internal water drainage system. If any water were to get past the membrane it will get caught by the channel system and be directed to the drain system. It has vertical and horizontal drainage every 10” to 12” where other systems must have drainage boards installed.

- Patented steel vertical track system allows drywall to meet 600’ of fire test. The drywall screws won’t melt out of plastic. They are attached to steel and the steel is attached to concrete.

- Reddi-Wall has available horizontal drywall attachment strips. Other brands do not have this option. This provides the option of attaching vertically or horizontally.

- Post and beam construction accommodates concrete shrinkage without allowing concrete to crack.  Other systems provide no expansion provision.

- Reddi-Wall has no sharp corners to cause stress concentrations that usually produce cracks.

- Reddi-Wall has no flat ties between opposite panels that act as a control joint to produce a crack.

- Reddi-Wall has a UL 2 hour burn through fire rating and 5 hour for structural fire rating.

- Reddi-Wall is designed to withstand earthquakes up to 7 on Reiter scale. Flexible design allows movement without destruction.

- One-piece construction prevents movement. Panel movement is a major problem, which results in walls shifting and hour glassing.  Also requires very little bracing and that is mostly for safety.

- Reddi-Wall has a top and bottom track system. This prevents movement and holds walls secure.  It also protects tabs and for multiple pours.

- Reddi-Wall has a patented wall assembly panel system. This wall is very easy and fast to erect. A typical modular basement usually requires less then 3 hours to erect with a 3-man crew.

- Reddi-Wall requires no parts assembly. It comes as a pre-assembled unit.  This saves a lot of time.

- Ridged assembly requires almost no alignment and fits every time with out adjustment. A great time saver and also requires less bracing.

- Built in electrical chases provide for code required depth there is no need to cut wall to install electric. Wire can be added later without destroying drywall.

- Block is USA made in Ohio and are in 1-foot increments. No metric system.

- Wall assemblies can be ordered with window frames, door frames and electric installed. They can also be ordered with water membrane installed.  This allows for fast accurate installation.

- Reddi-Wall is a truss wall system. A truss is always stronger then solid because the forces are prevented from concentrating at one point as all solid walls do. A truss is strong because the external forces cancel each out there.  Also, this wall cuts concrete use by 1/3 to ½ as compared to other walls.

- Reddi-Wall complies with new 2002 code requirements by providing a 5” Brick ledge. 4” for Brick plus air space.

- Reddi-Wall provides a drainage system to remove water from behind brick, which no other system has.

- Reddi-Wall provides a 2” frost cushion at Brick ledge that exceeds 1 ½ required.

- Reddi-Wall has a built in tape measure on the block in 1” increments.

- Reddi-Wall is marked for drywall attachment strips.

- Horizontal corner aluminum siding attaching provisions are provided.

- Reddi-Wall has flat external sides. No other system has. This is a patented manufacturing process.

- Reddi-Wall has over 1000 structures in Michigan alone.  It has received several recognitions for quality and achievements in energy and health issues.  For this reason it is certified for 10’ filling at one time.

- In independent tests Reddi-Wall exhibited the highest bursting strength by a large margin.

- Reddi-Wall is universal, there is no top or bottom, no right or left corner, it is a patent universal feature.

- Internal braces keep the walls very straight.

- Reddi-Wall’s drywall mounting strips are 5/8” back from the surface. On other blocks where drywall comes in direct contact with anchor strips there is a BTU loss. This results in a moisture build up on back of the drywall.

- The top of the wall can be easily trimmed to meet exact height requirements.

- Reddi-Wall costs less then all brands we know of.

- Built in radon venting for entire structure.

Reddi-Wall Inc.

1075 Rochester Road * Oakland MI. 48363

586-752-9161

www.reddi-wall.com